## Slide 1
AIM: Acoustic Inertial Measurement
For Indoor Drone Localization and Tracking
Yimiao Sun1, Weiguo Wang1, Luca Mottola2, Ruijin Wang3, Yuan He1
1 Tsinghua University
2 Politecnico di Milano and RI.SE Sweden
3 University of Electronic Science and Technology of China

## Slide 2: Emerging Indoor Drone Application
Indoor Warehouse
Inventory
Logistics
Surveillance

## Slide 3: Dilemma of Indoor Drone Tracking
IMU-based methods
suffer from signal distor-tion due to rich multipath on metal.
GPS-denied
Rich mutipath
Frequent NLoS
RF-based methods
suffer from target loss due to frequent NLoS.
suffer from error accumu-lation due to lack of absolute coordinate.
Infrared-based methods

## Slide 4: Our Method
An acoustics based inertial measurement working in both LoS and NLoS.
Mean Error
1.43m in LoS
1.89m in NLoS
Error Comparison
46% less than UWB in NLoS
57% less than GPS in outdoor

## Slide 5: Insight
Hovering Motion
Yaw Motion
Vertical Motion
Horizontal Motion
Different motions lead to unique dynamics of propellers and fuselage.

## Slide 6: Insight
Hovering Motion
Yaw Motion
Vertical Motion
Horizontal Motion
Unique dynamics of propellers lead to distinct acoustic features

## Slide 7: AIM Overview
 | Single Peak | Multiple Peak
Unstable DoA | Vertical linear motion | Horizontal linear motion
Stable DoA | Hovering motion | Yaw motion
Entirely passive scheme
No hardware modification
Work across LoS & NLoS
Scalable to arbitrary range
Acoustic Inertial Measurement
with both frequency and spatial domain
Frequency domain
Spatial domain

## Slide 8: Preliminary
The drag force:
The sound heard:
The sound can be quantified based on drone’s structure.
Notes: : Lift force
: Drag force
: Constants
: number of blades
: Rotation frequency
𝑇_𝑖^𝑣: Lift force
𝑇_𝑖^ℎ: Drag force
𝑘^ℎ/𝑘^𝑣: Constants
𝑛: number of blades
𝑓_𝑖: Rotation frequency

## Slide 9: Observation
Hovering Motion
Yaw Motion
Vertical Motion
Horizontal Motion
How to disambiguate motions with the same number of frequency band?

## Slide 10: Motion Identification Scheme
 | Single Peak | Multiple Peak
Unstable DoA | Vertical linear motion | Horizontal linear motion
Stable DoA | Hovering motion | Yaw motion
Frequency domain
Spatial domain
Disambiguate motions with information in spatial domain
How to find the exact coordinates ?

## Slide 11: Tracking Model
In both dynamic equations, the only unknown quantity is the height
more detail, please refer to our paper.

## Slide 12: Tracking in NLoS
Smoothed NLoS azimuth always indicates whether NLoS appears.
Stable azimuth
Unstable azimuth
Stable elevation
Unstable elevation
If NLoS == True:
Enable acoustic-based inertial measurement; #Frequency domain
Else
Enable acoustic-based inertial measurement; #Frequency domain
Enable DoA-based direction calibration; #Spatial domain
Notes: If NLoS == True:
Enable acoustic-based inertial measurement; #Frequency domain
Else
Enable acoustic-based inertial measurement; #Frequency domain
Enable DoA-based direction calibration; #Spatial domain

## Slide 13: Evaluation
Playback Speed: 3x
UWB Node
Infrared Camera
Baseline
6-Mic Array
4-Mic Array
Microphone Array
DJI mini 2 Quadcopter
Distance Marker
Experiment area
Horizontal motions:
Fly along the distance maker.
Keep vertical coordinates unchanged.
Vertical motions:
Climb or descent to a certain height.
Keeping horizontal coordinates unchanged.
(Sampling rate: 48kHz)
(Weight: 249g BPF: 328Hz)
(Fixed on the tripods)
(Imaged by the drone’s camera)
Notes: 这一页的连线是否有必要

## Slide 14: Overall Performance
LoS Scenarios
PLoS Scenarios
Variation of errors
NLoS Scenarios
AIM outperforms LinkTrack 46% in NLoS with a mean error of 1.89 m
AIM can constantly provide location updates when OptiTrack is down.

## Slide 15: Impact of Environment Noise
AIM is robust to moderate noise sources in the environment
50dB
55dB
60dB
65dB

## Slide 16: Deployment in Real Warehouse
AIM outperforms UWB in the real warehouse environment
Layout of the warehouse
Accuracy in different regions

## Slide 17: Scalability in Range and Outdoors
AIM can extend to any range yet accuracy never degrades drastically.
AIM can function outdoors and outperform GPS 57 % in 2D tracking .
Accuracy at different distances
Comparison with GPS outdoors

## Slide 18: Summary
AIM is the first-of-its-kind passive indoor drone tracking technique that works with a single 2D microphone array.
The core innovation is that we explore acoustics-based dynamics, which bridges the drone’s dynamics equations and acoustic features.
AIM is able to localize a drone in any range and layout, with the mean errors 46% less than UWB indoors and 57% less than GPS outdoors.

## Slide 19
19
19
Thank You!

## Slide 20
20
20
Thank You!
Weiguo Wang
Luca Mottola
Yuan He
Yimiao Sun
Ruijin Wang